## Slide 1
Single Ion Images & boxplots
(for the lists of interesting molecules)
Pre-processing and saving representative spectra
Each input file has the information regarding what to do with each dataset. E.g.: how many peaks to save in each datacube, which adducts to look for, which MVA to run.
Save data files (imzMLs & ibds) in folders by modality and polarity
Fill in an input file (excel) for each folder of data
Save a master script in a location of your choice
Each file by itself
A group of files
(if we wish to later on group them –the so called common axis approach)
Matching representative spectra with lists of interesting molecules and databases
Lists of interesting molecules
(always needed)
HMDB
(only needed when you run MVA)
Saving data cubes
One data cube per dataset (imzML) is saved.
Data cubes can be assembled together if needed, if we assure they have the same exact m/z axis, which is defined in step 3.
Data cubes comprise the m/z requested in the inputs files: X highest peaks plus those in the lists of interest.
1.1
1.2
2.1
3
3A
3B
4
4.1
4.2
With information regarding which folders of data need to be processed, which files within these folders, which main masks to use, which normalisations to save.
Fill in the 1st cell of the pipeline script
2.2
Tables with information about all potential assignments
(e.g. peak details, ppm errors, spectral features, ion images features, relationships between peak intensities across files)
5
MVAs
(PCA, k-means and NNMF (for a set of predefined k), NN-tsne (with k automatically defined based on the elbow method and/or for a set of predefined k)
6A
ROC analysis
(for the lists of interesting molecules)
Tissue only
(main mask; most times needed)
Sample specific
(e.g. WT, KRAS, etc.)
(semi-automated) ROI definition
6B
Once you have each individual sample ROI saved, you can build a grid with all the samples together. Once such grid is defined (in a function), you can run both MVAs and single ion images for this new data setup.
Simplified MVA outputs (e.g.: simplified version of those saved on the main pipeline; % of cluster cover by tissue)
Ratios of single ion images for the lists of interesting molecules
Pre-processing is done using each one of the main masks per dataset. So you have to do it at least twice: all pixels and tissue only pixels.
Each sample specific mask is part of a main mask. You should therefore define them at the time you define the main mask.
Normalisation is done at the main mask level.
7
7.1
7.2
Semi-Automated Data Processing Pipeline
Comments / Help
Working pipeline (been used by Chelsea)
Partially implemented but not ready to be used by everybody.
Running
Saving outputs (includes images of drivers)
6A.1
6A.2
Letters can be done in parallel
Numbers need to be done sequentially
It is recommended to have a master script for each study, as information regarding data location needs to be specified in it.

## Slide 2
f_saving_spectra_details( filesToProcess, preprocessing_file, mask_name )
Pre-Processing Data &
Saving Total Spectra
Semi-Automated Data Processing Pipeline
What we need?
Peak Picking &
Saving Peak Details
f_saving_peaks_details( filesToProcess, mask_name )
Peak Assignment
f_saving_relevant_lists_assignments( filesToProcess, mask_name )
f_saving_hmdb_assignments( filesToProcess, "no mask" )
Defining the list of m/z values that needs to be included in the datacube
Saving the datacube
f_saving_datacube_peaks_details( filesToProcess, mask_name )
f_saving_data_cube( filesToProcess, mask_name )
struct of files of interest - path to the SpectralAnalysis file for pre-processing – name of the mask defining pixels of interest
total spectral and related m/z values – number of pixels of interest
struct of files of interest - name of the mask defining pixels of interest - outputs of step 1
PeakDetails (list of all peaks found with the position of the centroids, the right and left limits of the peak, the total counts per peak)
What is saved?
struct of files of interest - pixels of interest mask - lists of names and monoisotopic masses of interest – hmdb – maximum ppm error - adducts
(all peaks within peak details and a given ppm error are assigned to a list of interest and/or hmdb identity)
2 tables of assignments are saved (one for the relevant lists and other for hmdb); these tables have up to 17 fields like adduct, ppm, name, database, class, mean counts, etc… These tables can be seen as a short version of PeakDetails (only peaks assigned to something are kept) with more information per peak
struct of files of interest - pixels of interest mask - the assignment tables + the numbers of top peaks + the percentiles + tables with the hmdb kingdoms/ classes/ etc.
struct of files of interest - pixels of interest mask - the vector with all m/z values that belong to anything requested in the inputs file
the vector with all m/z values that belong to anything requested in the inputs file
1
2
3
4
5
datacubes
Running the MVAs
Saving the outputs of MVAs
f_running_mva( filesToProcess, mask_name, list_of_normalisations, list_of_molecules_of_interest, list_of_molecular_classes_of_interest)
f_saving_mva_outputs ( filesToProcess, mask_name, mask_on_or_off_in_sii, list_of_normalisations, list_of_molecules_of_interest, list_of_molecular_classes_of_interest)
struct of files of interest - pixels of interest mask - what mvas to run (input files) - which peaks to use (inputs file + the two lists of strings that are arguments in this function)
struct of files of interest - pixels of interest mask - what mvas to run (input files) - which peaks to use (inputs file + the two lists of strings that are arguments in this function – weather we want to mask or not to mask the background of the single ion images
all matlab files that are necessary to plot the results are saved
6
7
maps and components are saved – sii for the 10 top loadings are saved – tables with the peaks that belong to each component are saved
Saving SIIs
f_saving_sii_relevant_molecules( filesToProcess, mask_name, mask_on_or_off_in_sii, list_of_normalisations, list_of_molecules_of_interest)
struct of files of interest - pixels of interest mask - lists of molecules of interest – weather we want to mask or not to mask the background of the single ion images
8
SIIs are saved in individual folders, one per list of molecules of interest
Steps 1 to 8 are usually done using the mask called “no mask”, i.e., using all the pixels of each imzML file.
Step 8 is not mandatory for any of the steps that follow.

## Slide 3
f_mask_creation( filesToProcess(file_index), input_mask, dataset_name, mva_type, numComponents, norm_type, vector_set, regionsNum2keep, regionsNum2fill, output_mask )
Manual Mask Creation
(whole tissue, specific tissues, tumour, background, etc.)
Semi-Automated Data Processing Pipeline
What we need?
done file by file so filesToProcess needs to have only one file – mask used to run the mvas that will be called – name of the dataset used (only valid for when many small regions are used to build a new “dataset” / also called the common axis approach – set to an empty vector otherwise) – what mva – num of components – what normalisation – which lusters – how many regions will be kept – how many regions will be filled – name of the new mask
folder called the new mask name with the SpectralAnalysis variable region of interest in it
What is saved?
9
Step 9 is usually done to create the “tissue only” mask and any other sample specific mask
f_saving_spectra_details( filesToProcess, preprocessing_file, mask_name )
Pre-Processing Data &
Saving Total Spectra
Peak Picking &
Saving Peak Details
f_saving_peaks_details_ca( filesToProcess, mask_name )
Peak Assignment
f_saving_relevant_lists_assignments_ca( filesToProcess, mask_name )
f_saving_hmdb_assignments( filesToProcess, "no mask" )
Defining the list of m/z values that needs to be included in the datacube
Saving the datacube
f_saving_datacube_peaks_details_ca( filesToProcess, mask_name )
f_saving_data_cube( filesToProcess, mask_name )
struct of files of interest - pixels of interest mask - path to the SpectralAnalysis file for pre-processing - mask of pixels of interest - path to the folder where all results will be saved
total spectral and related m/z values – pixels number for the given mask - height and width of the image
struct of files of interest - pixels of interest mask - total spectral and related m/z values - path to the folder where all results will be saved – the total spectra of all files in filesToProcess will be summed and the peak picking is done at the result of this sum
PeakDetails (list of all peaks found with the position of the centroids, the right and left limits of the peak, the total counts per peak) – the same exact PeakDetails are saved for all files
struct of files of interest - pixels of interest mask - lists of names and monoisotopic masses of interest – hmdb – maximum ppm error - adducts
(all peaks within peak details and a given ppm error are assigned to a list of interest and/or hmdb identity)
2 tables of assignments are saved (one for the relevant lists and other for hmdb); these tables have up to 17 fields like adduct, ppm, name, database, class, mean counts, etc… These tables can be seen as a short version of PeakDetails (only peaks assigned to something are kept) with more information per peak – the same exact tables are saved for all files
struct of files of interest - pixels of interest mask - the assignment tables + the numbers of top peaks + the percentiles + tables with the hmdb kingdoms/ classes/ etc.
struct of files of interest - pixels of interest mask - the vector with all m/z values that belong to anything requested in the inputs file
the vector with all m/z values that belong to anything requested in the inputs file – the same exact vector is saved for all files
10
11
12
13
14
datacubes
Steps 10 to 14 using the mask called “tissue only”, which is defined in step 9.

## Slide 4
Semi-Automated Data Processing Pipeline
What we need?
What is saved?
Running the MVAs
Saving the outputs of MVAs
f_running_mva_ca( extensive_filesToProcess, main_mask_list, smaller_masks_list, dataset_name, list_of_normalisations, list_of_molecules_of_interest, list_of_molecular_classes_of_interest)
f_saving_mva_ca( extensive_filesToProcess, main_mask_list, smaller_masks_list, dataset_name, list_of_normalisations, list_of_molecules_of_interest, list_of_molecular_classes_of_interest)
all outputs from step 15 - what mvas to run (input files) - which peaks to use (inputs file + the two lists of strings that are arguments in this function) – if list_of_molecules_of_interest and/ or list_of_molecular_classes_of_interest are empty, it is run for the lists in the inputs_file
all outputs from step 15 - what mvas to run (input files) - which peaks to use (inputs file + the two lists of strings that are arguments in this function) - if list_of_molecules_of_interest and/ or list_of_molecular_classes_of_interest are empty, it is run for the lists in the inputs_file
all matlab files that are necessary to plot the results are saved
16
17
maps and components are saved – sii for the 10 top loadings are saved – tables with the peaks that belong to each component are saved
Saving SIIs
f_saving_sii_relevant_molecules_ca( extensive_filesToProcess, main_mask_list, smaller_masks_list, outputs_xy_pairs, dataset_name, list_of_normalisations, list_of_molecules_of_interest)
OR f_saving_sii_ca( extensive_filesToProcess, main_mask_list, smaller_masks_list, outputs_xy_pairs, dataset_name, norm_list, sii_peak_list )
all outputs from step 15 – list of normalisations – list of molecules of interest
2nd function - it can accept hmdb classes, relevant molecules lists names or a vector of measured masses
19
SIIs are saved in individual folders, one per list of molecules of interest – barplots using the small mask are also saved
Defining a “New Dataset”,
comprising different imzMLs
[ extensive_filesToProcess, main_mask_list, smaller_masks_list, outputs_xy_pairs ] = f_studyX_samples_scheme_info( dataset_name, background, check_datacubes_size );
a unique function has been defined by study; this function specifies which files and smaller masks are to be located where, in a big grid – a name has to be given - whether the small masks have background or not (better to see function – this is not necessary) – if we want to check if all the datacubes have the same exact masses (this is necessary for any think to make sense in the future)
15
a lists of files paths – a list of main masks – a list of small masks – the position occupied by each small mask
Step 15 is necessary to create an arrangement of imzMLs.
Automated Mask Creation
using MVA outputs
f_saving_mva_rois_ca( extensive_filesToProcess, main_mask_list, dataset_name, mva_list, numComponents_list, list_of_normalisations, molecules_list )
Only works for mvas in which clusters are saved – the details of the mva need to be given, as well as which list was used to run that mva (molecules_lists is the string that is saved after the string mva in the folder with all the results)
18
Step 16 to 17 are optional.
Step 18 is optional.
Step 19 is optional.

## Slide 5
Semi-Automated Data Processing Pipeline
What we need?
What is saved?
T-test
f_saving_t_tests( extensive_filesToProcess, main_mask_list, group0, group0_name, group1, group1_name, norm_list )
all outputs from step 15 - define group 0 and 1, using the names of the small masks created in step 9, as described below:
Step 1:
WT_group = [ "SA1-2-WT","SA2-2-WT" ];
KRAS_group = [ "SA1-1-KRAS","SA1-2-KRAS","SA2-1-KRAS","SA2-2-KRAS" ];
APC_group = [ "SA1-1-APC","SA1-2-APC","SA2-2-APC" ];
APC_KRAS_group = [ "SA1-1-APC-KRAS","SA1-2-APC-KRAS","SA2-1-APC-KRAS","SA2-2-APC-KRAS" ];
Step 2:
group0 = WT_group;
group0_name = "colon WT";
group1 = [ KRAS_group, APC_group, APC_KRAS_group ];
group1_name = "colon not WT";
tables with p-values for two t-tests (standard and non-parametric), done for all m/z values saved in the datacube)
16
ROC
f_saving_roc_analysis( extensive_filesToProcess, main_mask_list, main_mask_on_or_not, group0, group0_name, group1, group1_name, list_of_normalisations, dataset_name, smaller_masks_list, outputs_xy_pairs )
all outputs from step 15 – decide if the main mask is to be used when plotting the sii – define group 0 and 1, using the names of the small masks created in step 9, as described below:
Step 1:
WT_group = [ "SA1-2-WT","SA2-2-WT" ];
KRAS_group = [ "SA1-1-KRAS","SA1-2-KRAS","SA2-1-KRAS","SA2-2-KRAS" ];
APC_group = [ "SA1-1-APC","SA1-2-APC","SA2-2-APC" ];
APC_KRAS_group = [ "SA1-1-APC-KRAS","SA1-2-APC-KRAS","SA2-1-APC-KRAS","SA2-2-APC-KRAS" ];
Step 2:
group0 = WT_group;
group0_name = "colon WT";
group1 = [ KRAS_group, APC_group, APC_KRAS_group ];
group1_name = "colon not WT";
20
list of areas under the curve (above 0.7 and below 0.3) for all m/z values in the datacube (with an additional column that tells you the potential database where that peak came from) – SIIs for all the m/z values show in the table
Steps 20 and 16 are optional.